## Slide 1
SESSION REPORT · 2026-06-07
Kria KV260 Bring-up
& CNN Inference Pipeline
End-to-end setup of the Xilinx AMD Kria KV260 Vision AI Starter Kit — from zero network access to running MobileNetV2 inference on-board.
SSH Connected
CNN Running
DPU — Next
YOLO — Planned
hemn · AMD Engineering

## Slide 2
Board Overview
HARDWARE
▸ Kria KV260 Vision AI Starter Kit
▸ SoC: Zynq UltraScale+ MPSoC
▸ CPU: Quad-core ARM Cortex-A53 @ 1.3GHz
▸ FPGA: PL fabric + AI Engine
▸ RAM: 4 GB LPDDR4
▸ Storage: 29 GB eMMC
SOFTWARE
▸ Ubuntu 24.04.4 LTS (Noble Numbat)
▸ Kernel: 6.8.0-1024-xilinx (aarch64)
▸ Python 3.12.3
▸ xmutil + dfx-mgr (overlay mgmt)
▸ fpga-manager-xlnx
▸ libxaiengine 2024.2
⚠ Ubuntu 24.04 is cutting-edge for Kria — Vitis AI apt packages officially target Ubuntu 22.04 and below.

## Slide 3
Challenge 1 — Network Discovery
PROBLEMS
▸ Host PC and Kria on different WiFi networks
▸ SSH (port 22) disabled by default
▸ mDNS kria.local didn't resolve
▸ Hostname xsjkria02x not in DNS
▸ Port scan: no open TCP ports found
RESOLUTION
▸ Physical access: opened terminal on board
▸ Connected both devices to same WiFi
▸ Board IP confirmed: 192.168.68.60
▸ TTL=64 on ping → Linux confirmed
# ARP scan on host
arp -a
# Wrong subnet initially:
192.168.1.116 64-ff-0a-85-f8-d2
# After switching WiFi:
ping 192.168.68.60
Reply: time=4ms TTL=64
# Enable SSH on Kria
sudo systemctl enable --now ssh
ip addr show # → 192.168.68.60

## Slide 4
SSH Key Authentication Setup
STEPS
▸ Enabled SSH on board via physical terminal
▸ Generated ED25519 key pair on host PC
▸ Copied public key to board's authorized_keys
▸ Verified passwordless login
✓ No password needed
✓ Automated iteration enabled
# Kria physical terminal
sudo systemctl enable --now ssh
# Host PC (PowerShell)
ssh-keygen -t ed25519 -f ~/.ssh/id_ed25519
type ~/.ssh/id_ed25519.pub | ssh \
ubuntu@192.168.68.60 \
"mkdir -p ~/.ssh && \
cat >> ~/.ssh/authorized_keys"
# Verify passwordless access
ssh ubuntu@192.168.68.60 "echo ok"
connected successfully ✓

## Slide 5
Software Stack Decision
❌ Vitis AI (apt)
▸ Not available for Ubuntu 24.04
▸ Targets Ubuntu 20.04/22.04
▸ No apt package found
❌ PYNQ
▸ pip install failed on Python 3.12
▸ Build error on aarch64
▸ Requires older Python
✅ ONNX Runtime
▸ Available for aarch64
▸ Supports Python 3.12
▸ Runs MobileNet/YOLO/ResNet
▸ Extensible to DPU EP
Installation: python3 -m venv ~/vitis-env && pip install onnxruntime numpy pillow

## Slide 6
CNN Inference Pipeline
MODEL
▸ MobileNetV2 — ImageNet (1000 classes)
▸ Format: ONNX | Size: 14 MB
▸ Input: 224×224 RGB
▸ Source: ONNX Model Zoo (official)
PIPELINE
▸ Load image → resize to 224×224
▸ Normalize (ImageNet mean/std)
▸ HWC → CHW → add batch dim
▸ ONNX Runtime inference session
▸ Softmax → Top-5 predictions
session = ort.InferenceSession(
"mobilenet.onnx",
providers=["CPUExecutionProvider"])
# Preprocess
img = Image.open("fish.jpg").resize((224,224))
x = np.array(img, dtype=np.float32)
x = (x/255.0 - mean) / std
x = x.transpose(2,0,1)[None]
# Infer
out = session.run(None, {"input": x})
top5 = np.argsort(out[0][0])[::-1][:5]

## Slide 7
Results — MobileNetV2 on Kria KV260
87.5 ms
INFERENCE TIME
14 MB
MODEL SIZE
1000
CLASSES
✓
WORKING
RUN DETAILS
Model
MobileNetV2-12 (ONNX)
Runtime
ONNX Runtime 1.26.0
Device
ARM Cortex-A53 (CPU)
Inference
87.5 ms
Top-1
tench ✓ (score: 17.54)
Status
End-to-end working ✓
Input: tench fish (ImageNet sample)
TOP-5
1. tench
17.54
2. snoek
11.21
3. coho salmon
10.44
4. bolete
10.28
5. goldfish
9.78

## Slide 8
Roadmap
✅ Phase 1 — Board Bring-up & CPU Inference
DONE
SSH setup · ONNX Runtime · MobileNetV2 · 87.5ms on ARM Cortex-A53
⚡ Phase 2 — DPU Acceleration
NEXT
Load DPU overlay via xmutil · ONNX DPU EP · Target: ~5–10ms (8–17× speedup)
🎯 Phase 3 — YOLO Object Detection
PLANNED
Quantize YOLOv8 INT8 with Vitis AI · Deploy on DPU · Live camera inference
🔬 Phase 4 — Custom HLS CNN
FUTURE
hls4ml: Keras → HLS C++ · Custom accelerator with Vitis HLS

## Slide 9
Key Learnings
TECHNICAL
▸ Ubuntu 24.04 on Kria is bleeding-edge — Vitis AI apt packages not yet available for Noble
▸ ONNX Runtime is a solid fallback for aarch64 inference without full Vitis AI stack
▸ xmutil + dfx-mgr is the correct path for DPU overlay management
▸ TTL=64 on ping quickly confirms Linux target
PROCESS
▸ Always verify host and target on same subnet before debugging SSH
▸ SSH key auth essential for automated remote iteration
▸ Physical board access saved significant time for initial setup
▸ Watch disk space — eMMC at 64% before Docker/model installs
Bottom line: Full CNN inference pipeline working on Kria KV260 in a single session. Next: DPU acceleration → 87ms → <10ms, then YOLO.