## Slide 1
AMD Kria KV260
Vision Robot Project
From Zero to Face-Detection + Servo Control in One Day
KV260 · Elegoo Mega 2560 · Ubuntu 24.04 · Python · OpenCV
June 2026

## Slide 2
🔧 Hardware Stack
All components and how they connect
🧠 KV260
AMD Kria KV260 — ARM Cortex-A53 + FPGA DPU | IP: 192.168.68.60 | Ubuntu 24.04
⚡ Elegoo Mega
Arduino Mega 2560 compatible — runs motor/servo control sketch
🔌 L298P Shield
4-channel motor driver — plugs ON TOP of Mega | 2A per channel | screw terminals
⚙️ TT DC Motors
2x TT Gear Motors (1:48 ratio, 3-6V) + wheels — press fit onto shaft
📷 USB Webcam
Logitech UVC | /dev/video0 | 640×480 | live inference at 12fps
🎛️ Elegoo Kit
SG90 Servo · HC-SR04 Ultrasonic · IR Remote · GY-521 IMU — all reused!

## Slide 3
🏗️ System Architecture
Full signal flow from camera to wheels
📷 USB Webcam /dev/video0 640×480
🧠 KV260 Python + OpenCV Face Detection
⚡ Elegoo Mega Arduino Sketch 9600 baud serial
⚙️ Left Motor
⚙️ Right Motor
🛞 Left Wheel
🛞 Right Wheel
frames
serial /dev/ttyACM0
PWM
PWM
L298P Motor Shield
🔌 USB Cable
🔋 AA Batteries → Shield → Motors 🔌 Wall Adapter → KV260

## Slide 4
✅ Proven Working — Day 1
Everything achieved in a single session
✅
SSH from Windows PowerShell → KV260
Fixed Sysnative path issue, added alias to PS profile
✅
Serial link: KV260 ↔ Elegoo Mega
/dev/ttyACM0 at 9600 baud — Hello from Elegoo confirmed
✅
Servo control from KV260
Python pyserial sends angles 0→90→180, servo moves on command
✅
USB Webcam detected on KV260
Logitech UVC on /dev/video0, 640×480 resolution
✅
Live object detection — MobileNetV2
~83ms/frame (12fps) on ARM CPU, detects couch/desk/person
✅
Face detection — Haar Cascade
OpenCV built-in, reliable at 1-2m distance
✅
FULL PIPELINE: Face → Serial → Servo
Webcam sees face → KV260 → Mega → servo sweeps 0→90→180→90→0

## Slide 5
🗺️ Development Roadmap
CPU-first approach — DPU when ready
✅ Phase 0
DONE
SSH · Serial · Servo · Webcam · Face Detection · Servo Sweep
🔜 Phase 1
PENDING
Motor control — KV260 drives 2x DC motors via L298P shield
🔜 Phase 2
PENDING
IR Remote control — drive robot with Elegoo IR remote
🔜 Phase 3
PENDING
Obstacle avoidance — HC-SR04 ultrasonic sensor
🔜 Phase 4
PENDING
Live webcam object detection on moving robot (CPU, 12fps)
🚀 Phase 5
FUTURE
YOLO on DPU — real-time 30fps AI vision (needs Ubuntu 22.04)
* Phases 1-4 run on Ubuntu 24.04 CPU only — no new microSD needed until Phase 5

## Slide 6
🛒 Shopping List
Everything needed — under $50 to get motors spinning
Microcenter Santa Clara — 5201 Stevens Creek Blvd
L298P 4-Channel Motor Drive Shield
~$30
Confirmed in stock
MicroSD Card 32GB+
~$10
For Ubuntu 22.04 flash (Phase 5)
Amazon
DIYmall 2x TT DC Gear Motor + 2 Wheels
~$10
Initial desk test — no chassis needed yet
XiaoR Geek Aluminum Tank Chassis 2WD
~$40
Future — after motors verified working
12V USB-C PD Power Bank
~$40
Future — for untethered robot operation
Raspberry Pi Camera v2
~$25
Future — for DPU-accelerated vision
Immediate total: ~$50 | Full robot total: ~$155

## Slide 7
🎯 Face Detection + Servo Demo
Working today — no DPU needed!
How it works:
1
Webcam captures frame
/dev/video0 → 640×480 image every 0.5s
2
Convert to grayscale
cv2.cvtColor(frame, COLOR_BGR2GRAY)
3
Haar Cascade face detection
haarcascade_frontalface_default.xml | minNeighbors=3 | minSize=30×30
4
Face found?
YES → trigger servo sweep | NO → keep scanning silently
5
Send angle commands to Mega
pyserial → /dev/ttyACM0 | 0 → 90 → 180 → 90 → 0
6
Mega moves servo
servo_test.ino | Serial.parseInt() | myServo.write(angle)
✅ Result: Face detected → servo sweeps 0→90→180→90→0 every 10 seconds. No face → stays still.

## Slide 8
🚀 Ultimate Goal
Autonomous vision robot powered by AMD DPU
The Final Robot
👁️ Sees
Camera captures live video → KV260 DPU runs YOLO at 30fps
🧠 Thinks
Detects: person / obstacle / object — decides what to do
⚙️ Acts
Sends motor commands → Mega → wheels move accordingly
🔄 Reacts
Follow person · avoid obstacle · drive toward target object
📡 Control
IR remote override · ROS2 navigation · autonomous exploration
💡 Think of it as a mini self-driving car — camera eyes, FPGA brain, Arduino muscles.