## Slide 1
Face Detection → Servo Control
Using AMD Kria KV260 + Elegoo Mega 2560
A working demo — built in one day

## Slide 2
📡 The Pipeline
📷 USB Webcam
🧠 KV260
👤 Face Detection
⚡ Elegoo Mega
🔄 Servo
→
→
→
→
/dev/video0 640×480
Ubuntu 24.04 Python + OpenCV
Haar Cascade ~83ms per frame
Arduino Sketch /dev/ttyACM0
Pin 9 SG90

## Slide 3
⚙️ How It Works
1
Webcam captures a frame
USB webcam plugged into KV260 → /dev/video0 → 640×480 image
2
Convert to grayscale
OpenCV converts color frame to grayscale for faster face detection
3
Run Haar Cascade detector
OpenCV built-in face model scans the frame — no GPU or DPU needed
4
Face found?
YES → send sweep command to Mega | NO → wait and scan again
5
Send angles over USB serial
Python pyserial writes 0, 90, 180, 90, 0 to /dev/ttyACM0 at 9600 baud
6
Servo sweeps
Elegoo Mega reads angles → moves SG90 servo — repeats every 10 seconds

## Slide 4
🔌 Hardware Wiring
📷 USB Webcam
↓ USB cable
🧠 KV260 192.168.68.60
↓ USB cable (/dev/ttyACM0)
⚡ Elegoo Mega 2560
🔌 Servo Wiring (SG90 → Mega)
Brown wire
→
GND pin on Mega
Red wire
→
5V pin on Mega
Orange wire
→
Pin 9 on Mega
🔄 SG90 Servo (sweeps 0 → 90 → 180 → 90 → 0)
💡 Key Notes
• Serial baud: 9600
• chmod 666 /dev/ttyACM0
• vitis-env python3
• Wait 3s after serial
open (Mega boot)
• Stand 1-2m from
webcam for detection
• Only 1 script can use
serial at a time

## Slide 5
✅ Demo Results
What happens when you walk in front of the camera:
✅ Face detected
"Face detected! (1 face(s))" — printed every 0.5 seconds
🔄 Servo sweeps
0° → 90° → 180° → 90° → 0° — smooth sweep in ~4 seconds
⏱️ Every 10 seconds
While face is visible, servo re-sweeps every 10 seconds
😶 No face → silent
When you walk away — servo stays still, camera keeps scanning
📊 Performance
~83ms per frame on ARM CPU · ~12fps · no GPU/DPU needed
🎉 Full pipeline working: Webcam → KV260 → Face Detection → Serial → Elegoo Mega → Servo Sweep